## Slide 1
KINECT AR
TECHNICAL COMPONENTS

## Slide 2
CLIENT 1
SERVER
CLIENT N
.
.
.
ACTORS

## Slide 3
CLIENT
SERVER
KINECT
Kinect SDK
Unity
SpaceBrew client
Kinect interface
SpaceBrew
Node.js
Unity
SpaceBrew client
Orientation manager
(AR module)
Gyroscope
DISPLAY
AR/VR
AR Library
CAMERA
COMPONENTS

## Slide 4
Requirements:
Hardware:
  Kinect v2
Software:
  Windows
  Unity
  Kinect SDK
  SpaceBrew
  Node.js
Role:
Inputs from Kinect:
  RGB image
  Depth image
  Bodies/skeletons
Process data
  Detect “collisions”
  Update global game state
Outputs to Client i:
  Position of Client i Head
  Position of Client i Hand(s)
  Relevant game data
Can be integrated in
Unity project
SERVER
KINECT
Kinect SDK
Unity
SpaceBrew client
Kinect interface
SpaceBrew
Node.js
SERVER

## Slide 5
For calibration?
CLIENT
Unity
SpaceBrew client
Orientation manager
(AR module)
Gyroscope
DISPLAY
AR/VR
AR Library
CAMERA
CLIENT
Requirements:
Hardware:
  Gyroscope
  Screen
  Camera
Software:
  Android
  Unity
  (AR Library)
Role:
Inputs from Server:
  Position of Head
  Position of Hand(s)
  Relevant game data
Process data
  Update local game state
  Update position
  Update orientation
  Display world
Outputs to Server:
(nothing)
  (Head orientation?)

## Slide 6
Position & Orientation:
  => Unity scene must be a close representation of real world
Position:
  - Provided body joints positions are relative to centre of Kinect sensor
=> Need to offset the objects:
      Use Kinect world centre as centre of the scene
      OR
      Position objects locally in a container located at Kinect’s position
      OR
      Add required offsets to each object’s position
Orientation:
  - Kinect and Unity scene should have same orientation
  => Same “up” & “right” vectors (not “forward”*)
      YAW = 0.0
      PITCH = 0.0
=> Make sure the Kinect is not tilted! (REMOVE/ADJUST STAND)
      ROLL = 0.0
SERVER – KINECT

## Slide 7
Position offset:
  Kinect position relative to centre of world, to be determined based on scene
Typical initial offset:
- X = 0.0
- Y = (Height from floor)
=> Hardcoded? Provided input? Automatically measured?
- Z* = 3.0 (meters) – (ideal)
=> Determine based on scene.
* – Kinect data is mirrored from real world, Z axis is facing the opposite direction!
=> Z values need to be inverted if mimicking real world
SERVER – KINECT

## Slide 8
Position:
  In scene: Provided by server from Kinect skeletal joints (body frames)
  In real world: Need to consider offset
  => Screen/VR headset offset in regards to head central position
  ? => How to determine?
  => Current world position + “offset” correctly oriented
Orientation:
  In real world: Provided by gyroscope (Android API)
  In scene: Need to be calibrated at initialisation
  ? => How to determine?
  => Initial scene orientation + current world orientation
CLIENT – HEAD
1
2

## Slide 9
Kinect head joint
Kinect head joint
Position offset:
  => Screen/VR headset offset in regards to head central position
  ΔX = 0.0 (unless camera not centered!)
  ! => To be tested/checked
  ΔY should be close to 0.0
  ! => To be tested/checked
  ΔZ to be measured
? => Can have same values for every player? Or based on height?
CLIENT – HEAD
1

## Slide 10
Orientation calibration:
  => Difference in orientations from device (world) and game (scene)
  YAW to be measured
  ? => AR? Manual/Automatic?
  PITCH: No need to calibrate => Scene aligned to world
  ! => Kinect must be properly aligned to world
  ROLL: No need to calibrate => Scene aligned to world
  ! => Kinect must be properly aligned to world
CLIENT – HEAD
2

## Slide 11
Kinect
Headset
Orientation calibration: YAW
  => 2 angles to consider:
  θW : Initial YAW from device
  => Arbitrary value from world
    (Given by gyroscope)
  θK : Initial YAW with Kinect
    => Can be measured if facing the Kinect
      - X & Z provided by head joint position
  => Ask user to look at Kinect
      Using overlay in headset display
      Allow some time to aim at target
      => Counter, 5-10 seconds
CLIENT – HEAD

## Slide 12
Orientation:
  YAW = YAWGYRO – θW + θK
  PITCH = PITCHGYRO
  ROLL = ROLLGYRO
! – Gyroscope axis system is oriented differently than Unity axis system!
=> Needs to be transformed accordingly
CLIENT – HEAD

## Slide 13
TODO!
Hand tracking
  => Using Kinect body frames
  ! – Tracking struggle when hands in front of body!
Could hold coloured devices to allow different types of interactions
  => Colour tracking with Kinect RGB image (using OpenCV?)
CLIENT – HANDS