## Slide 1: KINECT TRACKING
Basic overview of Kinect tracking features and possibilities

## Slide 2: CONTENT
KINECT OUTPUTS
COORDINATES SYSTEMS
TRACKING
UNITY SETUP
KINECT LIBRARIES
RESOURCES
REMARKS / OTHER POINTS

## Slide 3: KINECT OUTPUTS
Raw Data – Frames
  Colour frames
    From RGB camera
    1920 x 1080
     Can be used target tracking (colour or image)
  Depth frames
    From IR camera
    512 x 424
     Can be used for volume tracking
  Body frames
    List of bodies composed of joints
     Can be used for body tracking

## Slide 4: KINECT OUTPUTS
Body Tracking
  Can track up to six skeletons at one time
  A skeleton has 25 joints (numbered 0–24)
  A joint has 11 properties:
    Colour coordinates (x, y)
    Depth coordinates (x, y)
    Camera coordinates (x, y, z)
    Orientation coordinates (x, y, z, w)
     Quaternions

## Slide 5: COORDINATES SYSTEMS
Image coordinates (x, y)
  In Colour and depth images
  Origin (x=0, y=0) is the top left corner pixel of the image
  Kinect returns a value between 0 and 1 for the
   The values are percentages of a set scale of 0–1 based on the camera’s resolution

## Slide 6: COORDINATES SYSTEMS
Camera coordinates (x, y, z)
  Origin (x=0, y=0, z=0) is located at the centre of the IR sensor
  From the sensor’s POV:
    X grows to the sensor’s left
    Y grows up
     This direction is based on the sensor’s tilt!
    Z grows out in the direction the sensor is facing
  1 unit = 1 meter
   The depth range of the Kinect is eight meters, but the skeleton tracking range is 0.5m to 4.5m, and it has trouble finding a skeleton at closer than 1.5m because of the field of view of the camera. So the cameraZ value will usually fall somewhere between 1.5 and 4.5

## Slide 7: COORDINATES SYSTEMS
Orientation coordinates (x, y, z, w)
 Kinect uses quaternions to deliver joint orientation

## Slide 8: TRACKING
Kinect Tracking:
 Skeletal tracking handled by depth sensor
  Body tracking
   Up to 6 skeletons
  BUT: Should limit to 2-3 max
  Hands tracking
   Left/Right, Open/Close + gestures
  BUT: Limited due to occlusion/proximity
   Combine with image analysis?
  Head tracking
   Position of centre of head (around eyes level) and neck
  BUT: Orientation not reliable
   Combine with image analysis?
   Combine with external device tracking

## Slide 9: TRACKING
Additional Tracking
 Combine Kinect body tracking with image analysis
  Colour tracking
   Using OpenCV or similar image analysis library
  Image target tracking
   Using OpenCV or similar, or using an AR library?

## Slide 10: TRACKING
Additional Tracking
Benefits:
Enhance tracking in “difficult” cases
Allow “props” handling
BUT:
Very compute-intensive!
  Use optimisation techniques
 Sub-sampling, etc.
  Only analyse meaningful ROIs
 Areas covered by bodies

## Slide 11: TRACKING
Hands Tracking:
  Colour tracking
   Adapted if “spherical trackers” (e.g.: Sony PSMove)
  BUT: No orientation tracking
  Image target tracking
   Adapted if 2 hands holding, limited movement and orientation changes
  BUT: harder skeletal tracking

## Slide 12: TRACKING
Head Tracking:
  Colour tracking
   Adapted if “spherical trackers” (e.g.: Sony PSMove)
  BUT: No orientation tracking, so not really useful
  Image target tracking
   Adapted if facing camera
  BUT: Limited orientation changes
  Face recognition tracking
   Handled by Kinect , adapted if no head device
  BUT: No AR/VR

## Slide 13: TRACKING
Head Tracking:
  External device tracking
   AR and/or orientation sensors
  BUT: Combining data is tricky and unreliable?
   Could use “approximate” visuals ...

## Slide 14: TRACKING
Head Tracking:
 Tracking with AR on external handheld device
  Orientation tracking
   Using an AR library (e.g.: Vuforia) + image trackers
Provide head orientation tracking

## Slide 15: UNITY SETUP
 Main Microsoft Dev page:
https://developer.microsoft.com/en-us/windows/kinect
  Download Kinect SDK
  https://www.microsoft.com/en-us/download/details.aspx?id=44561
  Download Unity Pro package
   Mentions that need Unity Pro, but works with free Unity
  Connect the Kinect device
   Drivers will install automatically
  In Unity, import package:
  Kinect.2.0.1410.19000.unitypackage

## Slide 16: KINECT LIBRARIES
- MS Kinect SDK
https://www.microsoft.com/en-us/download/details.aspx?id=44561
!- OpenKinect/libfreenect2
=> Open source Kinect library
! - Good to get image data and feed OpenCV etc.!
https://openkinect.org/wiki/Main_Page
- Git page:
https://github.com/OpenKinect/libfreenect2
- API Reference:
https://openkinect.github.io/libfreenect2/
?- Kinectron
=> Open-source (?) framework to stream Kinect data...
https://kinectron.github.io/
- Could look at code (JS?)
!- Vitruvius Framework
=> Free version, 99$ for Unity support.
https://vitruviuskinect.com/
- Using Kinect & PS Move (or balls) for body tracking
=> Price?
https://www.driver4vr.com/
- OpenNI
https://structure.io/openni
=> Abandonned?
- Doc:
https://s3.amazonaws.com/com.occipital.openni/OpenNI_Programmers_Guide.pdf

## Slide 17: RESOURCES
Interesting resources
OpenCV:
Unity Asset
https://assetstore.unity.com/packages/tools/integration/opencv-for-unity-21088
BUT: Not free!
From sources
http://amin-ahmadi.com/2017/05/24/how-to-use-opencv-in-unity-example-project/
https://thomasmountainborn.com/2016/09/11/unity-and-opencv-part-one-install/
https://www.raywenderlich.com/5475-introduction-to-using-opencv-with-unity

## Slide 18: RESOURCES
Interesting resources
Kinect SDK Samples
 SDK Browser installed with Kinect SDK
MS Dev Portal - Kinect Forums
 SDK Browser installed with Kinect SDK
https://social.msdn.microsoft.com/Forums/en-US/home?forum=kinectv2sdk
GreenScreen
 Overlay texture data on body data (only tracked humans are displayed)
(Provided with the Unity Pro package from MS Kinect website)
BUT: BUG!
From:
https://unitycoder.com/blog/2016/09/29/using-xbox-one-kinect-with-unity/
 Fix shader in GreenScreen example:
https://forum.unity.com/threads/official-ms-kinect-unity-package-green-screen-shader-error.382295/#post-2484117
 Replace "SampleType" by "sampler_MainTex".
//sampler SampleType;
sampler sampler_MainTex;
...
//o = _MainTex.Sample(SampleType, i.tex);
o = _MainTex.Sample(sampler_MainTex, i.tex);
Kinect 2 Hands On Lab
 App similar to "GreenScreen" example (not Unity)
http://kinect.github.io/tutorial/lab05/index.html

## Slide 19: RESOURCES
Interesting resources
Understanding Kinect V2 Joints and Coordinate System
https://medium.com/@lisajamhoury/understanding-kinect-v2-joints-and-coordinate-system-4f4b90b9df16
Avateering with Kinect V2 – Joint Orientations
 "There are two main ways to represent body data from the Kinect:
  use the absolute positions provided by the SDK which are values in 3D Camera-space (in metres)
  use the joint orientation data to rotate a hierarchy of bones
The latter is the one we will look at here."
https://peted.azurewebsites.net/avateering-with-kinect-v2-joint-orientations/
  GitHub page:
https://github.com/peted70/kinectv2-avateer-jointorientations
Kinect 4 Windows V2 – Unity 3D
https://peted.azurewebsites.net/kinect-4-windows-v2-unity-3d/
 Old, still relevant?

## Slide 20: RESOURCES
Interesting resources
- Basic unity & kinect
https://www.youtube.com/watch?v=aHGlLxh6a88
- Avateering (kinect+unity)!
https://pterneas.com/2016/02/18/avateering-kinect/
- Lots of AR/VR articles/tutorials:
https://pterneas.com/
- KINECT COORDINATE MAPPING – THE EASY WAY
https://pterneas.com/2016/06/23/kinect-coordinate-mapping-vitruvius/
- MEASURING DISTANCES USING KINECT – THE RIGHT WAY
https://pterneas.com/2016/08/11/measuring-distances-kinect/
- KINECT JOINT ROTATION – THE DEFINITIVE GUIDE
https://pterneas.com/2017/05/28/kinect-joint-rotation/
=> BUT: uses Vitruvius?
!- Fast Color Based Object Tracking Using OpenCV and Kinect
https://imufeed.wordpress.com/2013/04/03/fast-color-based-object-tracking-using-opencv-and-kinect/
https://www.youtube.com/watch?v=d_c0Bqqvj6c
- Color Based Object Tracking Using Open Kinect and Processing
http://www.nbertagnolli.com/jekyll/update/2015/10/13/Object_Tracking.html

## Slide 21: REMARKS / OTHER POINTS
Remarks:
- vertical "bird-eye" view
=> Kinect doesn't recognise bodies, so would rely on image analysis only.
Related work: (people counting)
http://www.cbsr.ia.ac.cn/users/jjyan/XCZHANG-AVSS12.pdf
- Kinect is dead, MS advises to use Intel's RealSense cameras:
https://software.intel.com/realsense
Other points:
- HADO
=> outdoor video, how does it work?
- FeelReal:
=> interesting
https://www.kickstarter.com/projects/feelreal/feelreal