## Slide 1
KINECT AR
TECHNICAL COMPONENTS - BIS

## Slide 2
CLIENT
SERVER
KINECT
Kinect SDK
Unity
SpaceBrew client
Kinect interface
Tracking module
SpaceBrew
Node.js
Unity
SpaceBrew client
(Orientation manager)
DISPLAY
AR/VR
Gyroscope
COMPONENTS – REVISITED
CAMERA

## Slide 3
Requirements:
Hardware:
  Kinect v2
Software:
  Windows
  Unity
  Kinect SDK
  SpaceBrew
  Node.js
Role:
Inputs from Kinect:
  RGB image
  Depth image
  Bodies/skeletons
Process data
  Determine heads orientation
  Detect “collisions”
  Update global game state
Outputs to Client i:
  Position of Client i Head
  Orientation of Client i Head
  Position of Client i Hand(s)
  Relevant game data
Can be integrated in
Unity project
SERVER
KINECT
Kinect SDK
Unity
SpaceBrew client
Kinect interface
Tracking module
SpaceBrew
Node.js
SERVER

## Slide 4
For calibration?
CLIENT
Unity
SpaceBrew client
(Orientation manager)
DISPLAY
AR/VR
Gyroscope
CAMERA
CLIENT
Requirements:
Hardware:
  (Gyroscope)
    => Optional *
  Screen
  Camera
    => Display only
Software:
  Android
  Unity
Role:
Inputs from Server:
  Orientation of Head
  Position of Head
  Position of Hand(s)
  Relevant game data
Process data
  Update local game state
  Update position
  Update orientation
    => * Could combine with
    gyroscope data
  Display world
Outputs to Server:
(nothing)
  (Head orientation?)

## Slide 5
Position & Orientation:
  => Unity scene must be a close representation of real world
Position:
  - Provided body joints positions are relative to centre of Kinect sensor
=> Need to offset the objects:
      Use Kinect world centre as centre of the scene
      OR
      Position objects locally in a container located at Kinect’s position
      OR
      Add required offsets to each object’s position
Orientation:
  - Kinect and Unity scene should have same orientation
  => Same “up” & “right” vectors (not “forward”*)
      YAW = 0.0
      PITCH = 0.0
=> Make sure the Kinect is not tilted! (REMOVE/ADJUST STAND)
      ROLL = 0.0
SERVER – KINECT

## Slide 6
Position offset:
  Kinect position relative to centre of world, to be determined based on scene
Typical initial offset:
- X = 0.0
- Y = (Height from floor)
=> Hardcoded? Provided input? Automatically measured?
- Z* = 3.0 (meters) – (ideal)
=> Determine based on scene.
* – Kinect data is mirrored from real world, Z axis is facing the opposite direction!
=> Z values need to be inverted if mimicking real world
SERVER – KINECT

## Slide 7
Position:
  In scene: Provided by server from Kinect skeletal joints (body frames)
  In real world: Need to consider offset
  => Screen/VR headset offset in regards to head central position
  ? => How to determine?
  => Current world position + “offset” correctly oriented
Orientation:
  In real world: Provided by gyroscope (Android API)
    ! - Gyroscope not reliable! (esp YAW)
    => Compute from Kinect RGB images
  In scene: Need to be calibrated at initialisation
  => Relative to Kinect orientation
  => Initial scene orientation + current world orientation
CLIENT – HEAD
1
2

## Slide 8
Kinect head joint
Kinect head joint
Position offset:
  => Screen/VR headset offset in regards to head central position
  ΔX = 0.0 (unless camera not centered!)
  ! => To be tested/checked
  ΔY should be close to 0.0
  ! => To be tested/checked
  ΔZ to be measured
? => Can have same values for every player? Or based on height?
CLIENT – HEAD
1

## Slide 9
Orientation determination:
  => Using Kinect RGB video feed to determine head orientation
  YAW
  PITCH
  ROLL
=> PITCH & ROLL can be combined/validated with gyroscope data
  ! – Kinect must be properly aligned to world!
CLIENT – HEAD
2

## Slide 10
Orientation:
  => ... (TODO: explain Kinect image analysis method ...
CLIENT – HEAD
!!!! TODO !!!!

## Slide 11
HEAD TRACKING:
- Tracking using the Kinect:
=> Colour tracking in area around the head (area size related to distance from camera)
Process:
1 - Colour Segmentation - Blobs Detection
=> Biggest clusters of specific colours in RGB image.
2 - Positions Determination
=> From values in depth image at corresponding positions.
3 - Pose Estimation
=> Determine transformation from original model to found model.
(Only orientation is required, no position)
CLIENT – HEAD
!!!! TODO !!!!

## Slide 12
HEAD TRACKING:
Requirements:
- Hardware:
- Minimum 4 (3?) markers to determine the rotation matrix
- Markers need to be unique and easily trackable
=> Bright/luminescent colours.
- Markers physical layout must be deterministic
=> Combined ears and "mohawk"?
(Could use flashy 80s earpuffs)
- Players need to wear a special headset holding markers
- Players can't get out of Kinect FOV
(shouldn't anyway, as positioning will not work either)
=> If losing tracking, use the device's gyroscope? (How to manage?)
CLIENT – HEAD
!!!! TODO !!!!

## Slide 13
HEAD TRACKING:
Image Analysis Libraries:
AForge.NET (in C#):
  => How to integrate in Unity? How powerful? ...?
  http://www.aforgenet.com
  https://www.codeproject.com/Questions/738734/blob-detection-in-csharp
  http://www.emgu.com/forum/viewtopic.php?t=477
OpenCV:
  OpenCV Unity Asset
    https://assetstore.unity.com/packages/tools/integration/opencv-for-unity-21088
    => Not free!
  OpenCV from sources (via ++ DLL)
    https://thomasmountainborn.com/2016/09/11/unity-and-opencv-part-one-install/
    https://thomasmountainborn.com/2016/09/12/unity-and-opencv-part-two-project-setup/
    https://thomasmountainborn.com/2017/03/05/unity-and-opencv-part-three-passing-detection-data-to-unity/
    => Best way, but complex.
  OpenCV precompiled libraries (via C++ DLL)
    http://amin-ahmadi.com/2017/05/24/how-to-use-opencv-in-unity-example-project/
    => Easy and powerful – Need to check quality of libraries!
  OpenCV & Unity using sockets:
    https://github.com/hasanavi/OpenCV-Unity3D-Object-Tracking
    https://www.raywenderlich.com/5475-introduction-to-using-opencv-with-unity
    => Not ideal, as Kinect is already integrated in Unity.
CLIENT – HEAD
!!!! TODO !!!!

## Slide 14
HEAD TRACKING:
Colour Detection with OpenCV
  Colour tracking in Unity (using OpenCV plugin)
    https://handmap.github.io/opencv-colour-tracking-unity3d/
  Invisibility Cloak using Color Detection and Segmentation with OpenCV:
    https://www.learnopencv.com/invisibility-cloak-using-color-detection-and-segmentation-with-opencv/
  => Need to subscribe to download the code
  Blob detection with OpenCV SimpleBlobDetector:
    https://www.learnopencv.com/blob-detection-using-opencv-python-c/
    https://github.com/spmallick/learnopencv/tree/master/BlobDetector
    https://docs.opencv.org/3.4.3/d0/d7a/classcv_1_1SimpleBlobDetector.html
  Circular blob detection:
    https://riptutorial.com/opencv/example/22518/circular-blob-detection
  Fast Color Based Object Tracking Using OpenCV and Kinect:
    https://imufeed.wordpress.com/2013/04/03/fast-color-based-object-tracking-using-opencv-and-kinect/
    https://www.youtube.com/watch?v=d_c0Bqqvj6c
Object pose estimation
  => Might not need to use specific algorithms: only need to determine orientation from the different points.
CLIENT – HEAD
!!!! TODO !!!!

## Slide 15
...
Hand tracking
  => Using Kinect body frames
  ! – Tracking struggle when hands in front of body!
Could hold coloured devices to allow different types of interactions
  => Colour tracking with Kinect RGB image (using OpenCV?)
CLIENT – HANDS
!!!! TODO !!!!